## Slide 1: Please attribute as SimpleITK Fundamental Concepts (SPIE Medical Imaging 2019)
This work is copyrighted by the Insight Software Consortium
It is distributed under a Creative Commons Attribution 4.0 International License: https://creativecommons.org/licenses/by/4.0/

## Slide 2: SimpleITK Fundamental Concepts
Ziv Yaniv1,2 , Bradley C. Lowekamp1,2
1National Institutes of Health 2Medical Science and Computing LLC

## Slide 3: Transforms
All global transformation are of the form*:
*Except translation.

## Slide 4: Transforms
Free-Form Deformation:
You set:
  Spline order (default is cubic)
  Number of grid points per axis (mesh size)
  Spatial domain manually: origin; physical dimension; direction cosine matrix image based: BSplineTransformInitializerFilter
Transformation is identity outside the user defined domain.
sparse grid of control points with uniform spacing,
B0..3
cubic B-spline basis functions.

## Slide 5: Transforms
Displacement Field:
  Dense set of vectors representing the displacement in a given spatial domain.
You set:
  Spatial domain and deformation: manually: origin; physical dimension; direction cosine matrix; vector values. image based: vector image which is emptied of its contents.
Transformation is identity outside the user defined domain.

## Slide 6: Transforms
Composite transformation:
  Represents multiple transformations applied one after the other. T0(T1(T2(…Tn(p)...)))
Stack based semantics – first in last applied. composite_transform = sitk.Transform(T0) composite_transform.AddTransform(T1)
When used as the optimized transformation in registration (SetInitialTransform), only the parameters of the last transformation, Tn, are optimized.

## Slide 7: Images
An image is defined by:
  Pixel type + spatial dimensionality.
  Physical region in space occupied by the image as specified by: origin, spacing, size, and direction cosine matrix.

## Slide 8: Images
SimpleITK2Numpy:
  sitk.GetArrayFromImage – Data copied into numpy array (mutable).
  sitk.GetArrayViewFromImage – numpy array view of image data (immutable).
Numpy2SimpleITK:
  Copy bulk pixel data into SimpleITK image: new_image = sitk.GetImageFromArray
  Set all of the parameters defining the physical region in space:
    new_image.CopyInformation
    or
    new_image.SetOrigin, new_image.SetSpacing, new_image.SetDirection
Caution: If SimpleITK image is released the array view memory is no longer valid.

## Slide 9: Resample: Image + Transform
Resampling, three elements (assuming arbitrary interpolation method):
  Image – the image we resample in coordinate system m.
  transformation – T(fp) = mp maps points from coordinate system f to m.
  resampling grid – uniform set of points which will be mapped by the transformation.
f
m

## Slide 10: Resample: Image + Transform
Specifying the resampling grid
  Use an existing image.
  Use origin, size, spacing, and direction cosine.
f
m
Unexpected results: errors in resampling grid specification or transformation.

## Slide 11: Registration – Coordinate Systems
Three coordinate systems: Fixed, Virtual, Moving.
Three transformations: Tf(vp) = fp
Tm(vp) = mp
Topt(mp) = mp’
Most often Tf=I, the fixed and virtual coordinate systems coincide.

## Slide 12: Registration - Framework
Optimizers:
  Exhaustive
  Nelder-Mead Simplex/Amoeba
  Powell
  1+1 evolutionary
  GradientDescent GradientDescentLineSearch RegularStepGradientDescent
  ConjugateGradientLineSearch
  L-BFGS-B
  L-BFGS-2
Similarity metrics:
  MeanSquares Demons Correlation ANTSNeighborhoodCorrelation JointHistogramMutualInformation MattesMutualInformation
Multi-resolution framework.
Masks.
Sampling strategies.